## Slide 1: JUAS Xsuite tutorial: Collective effects
David Amorim, Elena de la Fuente Garcia, Sébastien Joly
The tutorial was inspired from the CAS Intensity Limitations in Hadron Beams ones (many thanks for the material!)

## Slide 2: Download files from github
https://github.com/JUAS-tutorials/collective-effects-xsuite-tutorials
Save the files:
  Code → git clone https://github.com/JUAS-tutorials/collective-effects-xsuite-tutorials.git
  Code → Download ZIP
Remember where you saved the files, you will need their location to open the notebook!

## Slide 3: Open notebook in jupyter lab
In Ubuntu, change directory to the folder where the files are located
Open jupyter lab
Paste the webpage address http://localhost:8888/lab?token=[...] to any browser

## Slide 4: Open notebook in jupyter lab and run it!

## Slide 5: Macro-particle tracking simulations

## Slide 6: HL-LHC wake model
The HL-LHC wake model includes the main wake contributors (vacuum chamber, collimators, vacuum instrumentation, beam dump, etc)
The wakefield produced by a particle can interact with its own bunch, the following or even turns later!

## Slide 7: Instability signature
Exponential growth of the bunch transverse position → bunch losses once it hits the vacuum chamber
Vacuum chamber ⌀ = 1 cm

## Slide 8: Task 1
Scan chromaticity (use big steps, stay within the range [-100,100]), when is the beam stable?
  Does the sign of chromaticity play a role?
  Is having a large chromaticity usually a good idea?

## Slide 9: Task 2
Scan the transverse feedback damping time (stay within the range [1,∞]), when is the beam stable?
  Which damper gain would be required to stabilize the beam for a Q' = 0?

## Slide 10: Task 3
Add the bellows’ impedance (modeled as a resonator), what happens?
Bonus: Replace the bellows by the shielded bellows’ impedance, what does it change?

## Slide 11: Notebook file structure

## Slide 12: Structure of the iPython notebook (1):importing libraries
Import xtrack, xpart, xwakes and xobjects from Xsuite
and import other required libraries and functions

## Slide 13: Structure of the iPython notebook (2): input parameters
Set machine and beam parameters
Machine circumference (in m)
LHC wake table
No acceleration
RF parameters

## Slide 14: Structure of the Python notebook (3): input parameters
Optics parameters
Transverse tunes
Momentum compaction factor
Initial bunch parameters
Bunch length
Number of macroparticles
Number of slices
Simulation parameters
Definition of bunch intensity scan
Number of simulated turns

## Slide 15: Structure of the iPython notebook (4):
Plot the input wakes
Import and configure wakes

## Slide 16: Structure of the iPython notebook (5):
Define segment map used for tracking
Create circular aperture
Enable particle losses (needed for beam loss plot)
Loop over
bunch
intensities
to be
scanned

## Slide 17: Structure of the iPython notebook (6):
Create one turn map
Create monitor
Loop over
bunch
intensities
to be
scanned

## Slide 18: Structure of the iPython notebook (7):
Track particles
Generate particles
Loop over
bunch
intensities
to be
scanned
Apply an initial kick to the distribution

## Slide 19: Structure of the Python notebook (7)
Plot average horizontal positions/intensity of
the bunch turn by turn

## Slide 20: ipython cheat sheet
To restart the kernel at any point: “Kernel” → “Restart”
To only interrupt the kernel: “Kernel” → “Interrupt”
Shift-enter: execute current cell and move to next cell
Ctrl-enter: execute current cell and stay on current cell